## Slide 1
PRINCIPLES OF FIELD SPECTROSCOPY • GEO-MSc-704
MODULE 4
Rigorous Field Sampling Protocols, Geometry & Quality Assurance
4 Teaching Hours • 1.5 ECTS Credits • 30 Lecture Slides
Module 4 bridges laboratory precision with the complex realities of outdoor field environments. MSc students master the geometry and physics of natural outdoor radiometry: restricting observations to the SZA < 45°–50° golden window, converting between civil time and true local solar time, and avoiding the optical retro-reflection hotspot. The module formulates sensor height and foreoptic footprint math, defines operator shadow/skylight exclusion zones, and establishes robust spatial sampling strategies (stratified random, regular grids, transects) for scaling up to Sentinel-2 and Landsat pixels. Students implement comprehensive metadata logging compliant with ISO 19115-2 and NERC FSF guidelines.

## Slide 2
MOD 4 • [PROTOCOL] • SLIDE 1/30
Introduction to Field Sampling Design & Geometrical Protocols
CORE TAKEAWAY: In situ optical radiometry is subject to dynamic outdoor environmental perturbations that require strict geometric and temporal sampling protocols.
Unlike laboratory benches, outdoor fields feature shifting solar angles, moving shadows, wind-induced canopy motion, and atmospheric aerosol variations.
Scientific reproducibility demands standardized geometrical constraints on illumination and viewing.
This module establishes the rules of engagement for outdoor data acquisition to ensure high-fidelity surface reflectance retrieval.
FIELD PROTOCOL NOTE
Flawed field protocol produces corrupted spectral signatures that no downstream algorithm can salvage.
References: Milton, E. J. et al. (2009). Progress in field spectroscopy. Remote Sensing of Environment, 113, S92-S109.
Notes: Welcome to Module 4. Here we transition from instrument mechanics to the operational choreography of outdoor field campaigns.

## Slide 3
MOD 4 • [PROTOCOL] • SLIDE 2/30
The Solar Zenith Angle (SZA) Window: The ±2 Hour Golden Window
CORE TAKEAWAY: Valid field spectroradiometry must be strictly confined to solar zenith angles θ_s < 45°–50° (within ±2 hours of local solar noon).
When θ_s > 50°, direct solar irradiance decreases rapidly, while optical air mass (AM) increases steeply.
High SZA elongates surface shadows, exaggerating non-Lambertian BRDF cavity scattering and micro-topographic shading.
High SZA causes forward specular scattering on Spectralon reference panels, introducing systematic calibration errors.
Golden Rule: Restrict primary field campaigns to between 10:00 and 14:00 true local solar time.
MATHEMATICAL FORMULATION
\theta_s \le 50^\circ \implies \text{Air Mass } m \le 1.55
Threshold ensuring high solar elevation and manageable atmospheric attenuation.
References: Curtiss, B., & Goetz, A. F. (1994). Field spectrometry: Techniques and instrumentation.
Notes: Show the solar elevation chart and emphasize why trying to acquire field spectra at 8:00 AM or 17:00 PM yields uninterpretable BRDF data.

## Slide 4
MOD 4 • [MATHEMATICS] • SLIDE 3/30
Local Solar Time vs. Civil Clock Time
CORE TAKEAWAY: Civil clock time differs substantially from true local solar time due to time zones, Daylight Saving Time, and orbital eccentricity.
Civil noon (12:00 on your watch) rarely coincides with true solar noon (maximum solar elevation).
Equation of Time (EoT): Accounts for Earth's orbital eccentricity and axial tilt (up to ±16 minutes shift).
Longitude correction: 4 minutes of time per degree of longitude away from the time zone meridian.
Always compute the exact solar noon timestamp using NOAA solar calculator algorithms before setting out.
MATHEMATICAL FORMULATION
\text{Solar Time} = \text{Civil Time} + \frac{4(\text{Lon} - \text{Lon}_{\text{ref}})}{60} + \frac{\text{EoT}}{60} - \text{DST}
Rigorous calculation of local solar time in hours.
References: Reda, I., & Andreas, A. (2004). Solar position algorithm. Solar Energy.
Notes: Walk students through calculating true solar noon for their exact university campus coordinates.

## Slide 5
MOD 4 • [PHYSICS] • SLIDE 4/30
Bidirectional Reflectance & The Optical Hotspot
CORE TAKEAWAY: When the illumination angle and viewing angle coincide (exact retro-reflection), shadows vanish, producing the optical hotspot.
Hotspot (opposition surge): Sharp peak in reflected radiance when looking directly along the solar illumination vector.
Physical causes: Complete disappearance of cast shadows behind foliage/soil particles + coherent backscatter.
Canopy reflectance can double within 2°–5° of the exact retro-illumination direction.
Avoid viewing geometries within 15° of the solar anti-solar point unless explicitly measuring hotspot parameters.
References: Kuusk, A. (1991). The hot spot effect of a plant canopy. In Photon-Vegetation Interactions, Springer.
Notes: Show aerial photos of the bright hotspot halo around an aircraft shadow over forests or crop canopies.

## Slide 6
MOD 4 • [PROTOCOL] • SLIDE 5/30
Viewing Geometry: Nadir vs. Off-Nadir Alignments
CORE TAKEAWAY: Standard ground validation requires strict nadir viewing (θ_v = 0°); unintended tilts introduce multi-percent BRDF errors.
Nadir viewing (0° zenith) looks straight down, matching typical satellite near-nadir swaths (e.g. Landsat, Sentinel-2).
A 5° tilt of the foreoptic towards the sun increases shadow exposure, artificially reducing apparent NIR reflectance.
A 5° tilt away from the sun captures illuminated leaf facets, artificially boosting reflectance.
Mandatory equipment: Two-axis bubble level mounted directly onto the foreoptic barrel.
FIELD PROTOCOL NOTE
Never trust human hand leveling; handheld foreoptics consistently drift by 6° to 12° during scans.
References: MacArthur, A. et al. (2014). Optimizing the use of field spectrometers. Remote Sensing of Environment.
Notes: Demonstrate with a laser pointer mounted on a handheld grip how much hand tremor shifts the target footprint.

## Slide 7
MOD 4 • [MATHEMATICS] • SLIDE 6/30
Calculating the Foreoptic Ground Footprint
CORE TAKEAWAY: The spatial sampling footprint is governed by sensor height, angular field of view, and viewing zenith angle.
For circular nadir foreoptics, the footprint is a circle of diameter D = 2 · h · tan(FOV / 2).
Footprint area scales with the square of height: A = π · (h · tan(FOV / 2))².
For off-nadir viewing (θ_v > 0°), the footprint elongates into an ellipse with major and minor axes governed by perspective projection.
MATHEMATICAL FORMULATION
D_{\text{nadir}} = 2 \cdot h \cdot \tan\left(\frac{\text{FOV}}{2}\right), \quad a = h \cdot \frac{\sin(\text{FOV}/2)}{\cos(\theta_v + \text{FOV}/2)}, \; b = h \cdot \frac{\sin(\text{FOV}/2)}{\cos(\theta_v - \text{FOV}/2)}
Circular nadir footprint and elliptical off-nadir footprint semimajor axes.
References: Curtiss, B., & Goetz, A. F. (1994). Field spectrometry techniques.
Notes: Have students calculate footprint sizes for 1°, 8°, and 25° foreoptics held at heights of 1 m, 2 m, and 5 m.

## Slide 8
MOD 4 • [PROTOCOL] • SLIDE 7/30
Target Footprint Sizing vs. Canopy Structural Scale
CORE TAKEAWAY: The footprint diameter must be at least 3 to 5 times larger than individual canopy structural elements to achieve representative averaging.
If footprint is smaller than a single leaf or gap: Measurements fluctuate wildly between 100% sunlit leaf and 100% dark shadow gap.
Representative Elementary Volume (REV): The minimum footprint size that yields a stable spatial average of canopy architecture.
In row crops (e.g. maize, vineyards), footprint must span an integer number of crop rows and inter-row spaces to prevent row-phase bias.
FIELD PROTOCOL NOTE
For 1 m tall agricultural crops, mount the 25° foreoptic at least 2.5 m above the top of the canopy.
References: Milton, E. J. (1987). Principles of field spectroscopy. International Journal of Remote Sensing.
Notes: Draw the REV graph: variance is huge at small scale, drops to a stable plateau, then rises as regional landscape heterogeneity enters.

## Slide 9
MOD 4 • [PROTOCOL] • SLIDE 8/30
Operator Exclusion Zone & Cast Shadows
CORE TAKEAWAY: The field operator and metallic equipment must remain outside the direct solar line and diffuse field of view.
Direct cast shadow: An operator standing between the sun and the target casts an obvious dark shadow, ruining the scan.
Diffuse sky obstruction: An operator standing near the target blocks a fraction of the 2π diffuse skylight, creating a subtle 2–5% blue deficit.
Clothing reflection: A bright yellow, red, or white jacket reflects colored photons onto the target or reference panel.
Standard rule: Operators must wear matte, non-reflective neutral gray or dark clothing and stand opposite or perpendicular to the solar azimuth.
FIELD PROTOCOL NOTE
Operator must stand at least 1.5 to 2.0 meters back from the target, aligned perpendicular to the solar principal plane.
References: NERC FSF (2020). Best Practice Manual for Field Spectroradiometry.
Notes: Show the polar diagram of diffuse sky blockage caused by an operator standing 50 cm away from a Spectralon panel.

## Slide 10
MOD 4 • [MATHEMATICS] • SLIDE 9/30
The Solar Principal Plane and Cross-Principal Plane
CORE TAKEAWAY: Anisotropy is maximum along the Solar Principal Plane and minimum along the Cross-Principal Plane.
Solar Principal Plane (SPP): Vertical plane containing the solar vector and the surface normal (azimuths φ = φ_s and φ = φ_s + 180°).
Contains both the optical hotspot (retro-reflection) and forward specular scattering peak.
Cross-Principal Plane (CPP): Vertical plane perpendicular to the SPP (azimuths φ = φ_s ± 90°).
BRDF variation is most symmetric and minimal in the Cross-Principal Plane, making it ideal for directional calibration tests.
References: Schaepman-Strub, G. et al. (2006). Remote Sensing of Environment, 103(1), 27-42.
Notes: Draw the 3D spherical coordinate geometry showing the SPP and CPP orientations relative to solar position.

## Slide 11
MOD 4 • [MATHEMATICS] • SLIDE 10/30
Spatial Heterogeneity & Sample Size Determination
CORE TAKEAWAY: The required number of field spectra depends statistically on target spatial variance and the desired margin of error.
Central Limit Theorem: The standard error of the mean decreases with the square root of sample size: SE = s / √N.
For a 95% confidence interval with allowable relative margin of error E: N = (t_crit · CV / E)², where CV is coefficient of variation (s / x̄).
In uniform wheat fields, N = 10–15 spectra may suffice; in heterogeneous rangelands, N = 50–100 spectra are required.
MATHEMATICAL FORMULATION
N = \left( \frac{z_{1-\alpha/2} \cdot \text{CV}}{E} \right)^2
Sample size formula for estimating population mean reflectance within relative tolerance E.
References: Cochran, W. G. (1977). Sampling Techniques (3rd ed.). John Wiley & Sons.
Notes: Work through an example: If CV = 20% and we want mean reflectance estimated within 5% error, N = (1.96 * 0.20 / 0.05)^2 ≈ 62 samples.

## Slide 12
MOD 4 • [PROTOCOL] • SLIDE 11/30
Sampling Strategies: Stratified Random vs. Systematic Grids
CORE TAKEAWAY: Spatial sampling designs must avoid sampling bias to represent true landscape pixel compositions accurately.
Simple Random Sampling: Every ground point has an equal chance of selection; avoids spatial autocorrelation bias.
Stratified Random Sampling: Divides heterogeneous field into homogeneous strata (e.g. hill crest, slope, hollow) and samples each proportionally.
Systematic Regular Grid: Evenly spaced grid nodes; guarantees uniform spatial coverage across satellite pixel footprints.
Cross-Transects (Star / X-shape): Rapid collection covering major directional gradients across a 30m × 30m pixel.
References: McCoy, R. M. (2005). Field Methods in Remote Sensing. Guilford Press.
Notes: Compare the four sampling diagrams and discuss when stratified random is superior to systematic grids.

## Slide 13
MOD 4 • [CASESTUDY] • SLIDE 12/30
Satellite Pixel Validation: Upscaling to Sentinel-2 and Landsat
CORE TAKEAWAY: Validating a 10m Sentinel-2 or 30m Landsat pixel requires integrating multi-point ground spectra weighted by Point Spread Function (PSF).
A single point spectrometer footprint (0.5 m) covers < 0.25% of a 10m × 10m Sentinel-2 pixel area (100 m²).
Point Spread Function (PSF): Satellite pixels are not square boxcars; the optical system weights central radiance higher than edges.
Field sampling must distribute 20 to 50 spectral points across the satellite Elementary Sampling Unit (ESU) centered on high-precision GNSS coordinates.
MATHEMATICAL FORMULATION
\bar{\rho}_{\text{pixel}}(\lambda) = \frac{\sum_{i=1}^N \text{PSF}(x_i, y_i) \cdot \rho_i(\lambda)}{\sum_{i=1}^N \text{PSF}(x_i, y_i)}
PSF-weighted spatial aggregation of point field spectra to satellite pixel scale.
References: Baret, F. et al. (2006). VALERI: A network of sites and a methodology for the validation of medium spatial resolution land products.
Notes: Show the Gaussian 2D PSF of Sentinel-2 MSI and how off-center ground targets contribute to adjacent pixels.

## Slide 14
MOD 4 • [PROTOCOL] • SLIDE 13/30
High-Precision GNSS Georeferencing in the Field
CORE TAKEAWAY: Standard smartphone GPS (±5 m error) is unacceptable for validating 10m satellite pixels; RTK-GNSS (±2 cm) is mandatory.
A 5-meter positional error places the validation sample into an adjacent agricultural field or road boundary.
Real-Time Kinematic (RTK) GNSS: Uses base-station carrier-phase differential corrections to achieve 1–2 cm horizontal precision.
PPK (Post-Processed Kinematic): Logs raw satellite observables for post-survey processing when cell coverage is absent.
Log GNSS coordinate at every spectral sampling station and record antenna height and horizontal dilution of precision (HDOP).
FIELD PROTOCOL NOTE
Wait for RTK Fixed status before logging waypoint; never accept RTK Float or autonomous GPS fixes.
References: Hofmann-Wellenhof, B. et al. (2008). GNSS – Global Navigation Satellite Systems. Springer.
Notes: Explain the difference between RTK Fixed (integer ambiguity resolved, cm accuracy) and RTK Float (decimeter uncertainty).

## Slide 15
MOD 4 • [QUALITYASSURANCE] • SLIDE 14/30
Continuous Illumination Monitoring: Pyranometers & Sky Radiometers
CORE TAKEAWAY: Deploying a continuous solar pyranometer station concurrent with field scans detects sub-visual cloud transients.
A dedicated pyranometer logging global solar irradiance at 1-second intervals provides an objective atmospheric stability record.
Irradiance coefficient of variation: CV_solar = σ(E) / μ(E) evaluated over 60-second sliding windows.
Quality threshold: Flag and discard field spectral scans acquired when CV_solar > 0.5% over the measurement duration.
FIELD PROTOCOL NOTE
Set the pyranometer logger on a small tripod in the center of the field site, connected via Bluetooth or SD card.
References: MacArthur, A. et al. (2014). Remote Sensing of Environment.
Notes: Show how a passing thin cirrus cloud creates a 3% dip in pyranometer flux that is invisible to the naked eye.

## Slide 16
MOD 4 • [INSTRUMENTATION] • SLIDE 15/30
Aerosol Optical Depth (AOD) Tracking with Sun Photometers
CORE TAKEAWAY: Handheld sun photometers (Microtops II) track instantaneous aerosol optical depth and total precipitable water column.
Microtops II: Five-channel handheld sun photometer pointed directly at the solar disk.
Measures direct solar irradiance at 380, 440, 675, 870, and 936 nm.
Retrieves AOD at 500 nm (τ₅₀₀) and water vapor column (W in cm) via Langley plot calibration.
CEOS WGCV requirement: Field campaigns must log AOD < 0.20 to guarantee clear-sky calibration quality.
FIELD PROTOCOL NOTE
Align the sun's image onto the Microtops alignment target with steady hands and take triplets of readings.
References: Morys, M. et al. (2001). Design, calibration, and performance of Microtops II handheld sunphotometer. Journal of Geophysical Research.
Notes: Introduce the Microtops instrument and show how AERONET data can substitute if a fixed site is within 25 km.

## Slide 17
MOD 4 • [QUALITYASSURANCE] • SLIDE 16/30
Environmental Covariates: Soil Moisture, Air Temp & Humidity
CORE TAKEAWAY: Spectra are meaningless without concurrent documentation of auxiliary biophysical and environmental covariates.
Soil moisture: Volumetric Water Content (VWC %) measured with TDR / FDR impedance probes in the top 5 cm.
Surface temperature: Thermal infrared radiometer (e.g. Apogee IRT) measuring target kinetic temperature.
Meteorological covariates: Air temperature, relative humidity, wind speed, barometric pressure logged with portable weather station.
FIELD PROTOCOL NOTE
Surface soil drying during a 4-hour midday campaign increases soil reflectance at 1600 nm by up to 15%.
References: McCoy, R. M. (2005). Field Methods in Remote Sensing.
Notes: Explain how neglecting soil moisture changes during a day can lead to false conclusions about vegetation growth.

## Slide 18
MOD 4 • [PROTOCOL] • SLIDE 17/30
Vegetation Canopy Structural Metrics: LAI and Leaf Angle
CORE TAKEAWAY: Canopy reflectance is strongly governed by Leaf Area Index (LAI) and Leaf Angle Distribution (LAD).
Leaf Area Index (LAI): Total one-sided leaf area per unit ground surface area [m² / m²].
Measure LAI concurrently using digital hemispherical photography (DHP) or plant canopy analyzers (LI-COR LAI-2200C).
Leaf Angle Distribution: Planophile (horizontal), erectophile (vertical), spherical, or plagiophile.
Erectophile canopies (grasses) show deep photon penetration and high shadow fractions at low SZA.
Planophile canopies (sunflower, clover) saturate reflectance at lower LAI values.
References: Jonckheere, I. et al. (2004). Review of methods for in situ leaf area index determination. Agricultural and Forest Meteorology.
Notes: Show photos of an erectophile grass canopy vs planophile clover and contrast their nadir reflectance spectra.

## Slide 19
MOD 4 • [PROTOCOL] • SLIDE 18/30
Leaf Sampling Protocols: Top-of-Canopy vs. Understory
CORE TAKEAWAY: When collecting foliar contact probe spectra, sampling must follow standardized vertical canopy stratification.
Sunlit top-of-canopy leaves have higher nitrogen, higher chlorophyll a/b ratio, thicker cuticles, and more palisade parenchyma layers.
Shade leaves have higher specific leaf area (SLA) and lower overall reflectance in the NIR.
Protocol: Collect fully expanded, healthy leaves from the upper outer sunlit crown (sun leaves) using pole pruners.
Wrap detached petioles in moist paper towels, seal in dark zip-bags on blue ice, and measure within 2 hours.
FIELD PROTOCOL NOTE
Never let leaves wilt or dehydrate before contact probe measurement; cell collapse alters NIR scattering instantly.
References: Doughty, C. E. et al. (2011). Foliar spectral traits in tropical trees. Remote Sensing of Environment.
Notes: Discuss proper leaf preservation techniques for remote expeditions.

## Slide 20
MOD 4 • [PROTOCOL] • SLIDE 19/30
Soil Surface Preparation Protocols: Roughness and Crusts
CORE TAKEAWAY: Surface crusts, tillage furrows, and gravel lag deposits dictate soil directional reflectance and micro-shadowing.
Micro-relief and surface roughness cast micro-shadows that reduce overall spectral reflectance (darkening effect).
Biological soil crusts (biocrusts): Cyanobacteria, lichens, and mosses produce distinct chlorophyll absorption features on soil surfaces.
Protocol: Document whether the soil surface is undisturbed, crusted, ploughed, or freshly raked.
If collecting soil for laboratory spectroscopy, follow ISO 18400 sampling and dry sieving protocols (< 2 mm).
References: Ben-Dor, E. et al. (1999). Imaging spectrometry for soil applications. Remote Sensing of Environment.
Notes: Show how biological soil crusts in drylands produce a false "vegetation" signal due to cyanobacterial chlorophyll.

## Slide 21
MOD 4 • [PROTOCOL] • SLIDE 20/30
Aquatic and Water Surface Protocols: Above-Water Radiometry
CORE TAKEAWAY: Water surface radiometry requires precise viewing angles (θ_v = 40°, φ_rel = 135°) to avoid direct sun glint.
Mobley (1999) protocol: Aim foreoptic at water surface at viewing zenith angle θ_v = 40° and relative azimuth angle Δφ = 135° from the sun.
Measure water radiance L_t, sky radiance L_sky (at θ_sky = 40°), and downwelling irradiance E_s.
Water-leaving radiance: L_w = L_t - ρ_sky · L_sky, where ρ_sky is the Fresnel surface reflectance factor (typically 0.028 for calm water).
MATHEMATICAL FORMULATION
R_{\text{rs}}(\lambda) = \frac{L_w(\lambda)}{E_s(\lambda)} = \frac{L_t(\lambda) - \rho_{\text{sky}} L_{\text{sky}}(\lambda)}{E_s(\lambda)}
Remote Sensing Reflectance (R_rs) [sr⁻¹] for aquatic optical applications.
References: Mobley, C. D. (1999). Estimation of the remote-sensing reflectance from above-surface measurements. Applied Optics.
Notes: Point out why measuring water straight down (nadir) fails: severe sun glint blinds the spectrometer.

## Slide 22
MOD 4 • [INSTRUMENTATION] • SLIDE 21/30
Field Goniometers: Measuring Multi-Angular BRDF Outdoors
CORE TAKEAWAY: Field goniometers rotate a spectrometer foreoptic across a hemispherical arc to map surface anisotropy in situ.
Examples: FIGIFIGO (Finnish Geodetic Institute), ASG (Airborne Spectrometer Goniometer), MUFIGO.
Acquires reflected radiance across multiple view zenith angles (0° to 70°) and azimuth angles (0° to 360°).
Requires rapid automated acquisition (< 10 minutes) before solar position shifts significantly.
Provides empirical BRDF kernels used to calibrate MODIS and satellite BRDF/albedo products.
References: Suomalainen, J. et al. (2009). FIGIFIGO—A new Brazilian-Finnish field goniometer system. Sensors.
Notes: Show video/photos of the FIGIFIGO goniometer operating over snow and peat bogs.

## Slide 23
MOD 4 • [CASESTUDY] • SLIDE 22/30
Drone / UAV Pre-Survey Reconnaissance
CORE TAKEAWAY: Deploying a high-resolution RGB drone before ground spectroscopy maps micro-spatial heterogeneity and guides sampling strata.
Fly a preliminary 15-minute drone orthophoto survey at 30 m altitude (GSD < 1 cm).
Generate instant NDVI and elevation models to identify canopy gaps, bare soil patches, and vegetation vigor gradients.
Delineate homogeneous strata and assign optimal GPS waypoints for ground spectrometer operators.
FIELD PROTOCOL NOTE
Store the drone orthomosaic on field tablets for real-time navigation to sampling stations.
References: Anderson, K., & Gaston, K. J. (2013). Lightweight unmanned aerial vehicles will revolutionize spatial ecology. Frontiers in Ecology.
Notes: Highlight how UAV reconnaissance prevents wasting field time on non-representative ground patches.

## Slide 24
MOD 4 • [QUALITYASSURANCE] • SLIDE 23/30
Metadata Standards: ISO 19115-2 & FGDC Extensions
CORE TAKEAWAY: Data without standardized metadata is scientifically useless; ISO 19115-2 defines geospatial imagery and gridded data schemas.
ISO 19115-2: Geographic information — Metadata — Part 2: Extensions for acquisition and processing.
Mandatory sections: Lineage, instrument identification, platform characteristics, acquisition geometry, environmental conditions.
Machine-readable metadata: XML and JSON schemas enabling automated ingestion into global spectral repositories (SPECCHIO, ECOSTRESS).
References: ISO (2019). ISO 19115-2:2019 Geographic information — Metadata — Part 2. International Organization for Standardization.
Notes: Review the hierarchical tree structure of an ISO 19115-2 metadata document.

## Slide 25
MOD 4 • [QUALITYASSURANCE] • SLIDE 24/30
The NERC FSF Field Metadata Protocol
CORE TAKEAWAY: The Natural Environment Research Council Field Spectroscopy Facility defines the gold-standard operational field logging template.
Standard field sheet tracks 28 mandatory parameters per sampling station.
Includes: Campaign code, site name, instrument serial number, foreoptic ID, white reference ID, target description.
Optical parameters: Time (UTC), solar zenith, solar azimuth, sensor height, view zenith, view azimuth.
Environmental logs: Sky clarity (oktas), cloud types, wind speed, relative humidity, air temperature.
FIELD PROTOCOL NOTE
Complete every field sheet field in ink at the moment of acquisition; never reconstruct metadata from memory at the hotel.
References: NERC FSF (2020). Field Spectroscopy Protocol and Recording Template.
Notes: Distribute printable NERC FSF field sheets and review their layout.

## Slide 26
MOD 4 • [INSTRUMENTATION] • SLIDE 25/30
Digital Field Logging Systems: Mobile Apps & Electronic Tablets
CORE TAKEAWAY: Ruggedized field tablets with synchronized digital logging eliminate transcription errors and automatically tag GNSS and timestamps.
Digital tools: QField, ArcGIS Survey123, Fulcrum, or custom SPECCHIO mobile logging apps.
Direct Bluetooth sensor integration: Auto-populates GPS coordinates, compass heading, and digital photo into the spectral database.
Instant validation: Software validates that solar zenith is within bounds and alerts operator if time since last WR exceeds 5 minutes.
References: Hueni, A. et al. (2009). The spectral database SPECCHIO for improved data sharing and data analysis. Computers & Geosciences.
Notes: Demonstrate how an electronic form ensures no required parameter is accidentally skipped.

## Slide 27
MOD 4 • [PROTOCOL] • SLIDE 26/30
Target Site Photography: Contextual and Nadir Imagery
CORE TAKEAWAY: Every spectral target must be paired with high-resolution nadir and oblique contextual photography.
Nadir target photo: Taken looking straight down with a scale bar / ruler and color calibration checker (e.g. Macbeth card) in frame.
Allows automated digital image classification of fractional cover (green leaf %, brown litter %, bare soil %).
Four-cardinal-direction contextual photos: North, East, South, West views from the station to document surrounding terrain.
Sky condition photo: 180° fish-eye or wide-angle sky photo showing cloud cover status at time of scan.
FIELD PROTOCOL NOTE
Position the scale bar on the edge of the target footprint, never inside the active field of view.
References: CEOS WGCV (2014). Field Spectrometry Protocol.
Notes: Show how a photograph taken 5 years ago helped resolve an unexpected spectral anomaly in a long-term ecological study.

## Slide 28
MOD 4 • [PROTOCOL] • SLIDE 27/30
Field Team Logistics, Roles and Safety Choreography
CORE TAKEAWAY: A two-person field crew with distinct, synchronized roles operates 3x faster and with significantly fewer protocol errors.
Role 1 (Instrument Operator): Manages foreoptic pistol grip/boom, maintains nadir level, aims precisely, wears dark clothing.
Role 2 (Data Logger & Navigator): Controls computer/tablet, monitors real-time spectrum, tracks time since last WR, logs environmental data.
Communication: Verbal callouts ("Optimizing", "White Reference Acquired", "Scanning Target 1 of 5", "Save Complete").
Field safety: Heat stress mitigation, hydration, snake/insect protection, and vehicle communications in remote terrains.
FIELD PROTOCOL NOTE
Rotate roles every 2 hours to maintain sharp attention and prevent operator physical fatigue.
References: NERC FSF (2020). Operational Field Guide.
Notes: Run a mock drill in the classroom simulating the two-person team verbal communication sequence.

## Slide 29
MOD 4 • [QUALITYASSURANCE] • SLIDE 28/30
Post-Field Data QA/QC Triage Protocol
CORE TAKEAWAY: Execute systematic data triage immediately at the end of each field day while field conditions remain fresh in memory.
Step 1 (Integrity check): Verify file count matches field log sheets; confirm no corrupted or 0-byte files.
Step 2 (Visual screening): Plot all spectra in batch; immediately flag and isolate outliers with spurious slopes or clipping.
Step 3 (WR verification): Inspect WR check files; ensure maximum departure from 1.0 is < 1.5%.
Step 4 (Backup redundancy): Implement the 3-2-1 backup rule: 3 copies, 2 different media (laptop + external SSD), 1 cloud/remote copy.
FIELD PROTOCOL NOTE
Never wipe instrument memory cards until two verified backups have been completed and checked.
References: Wilkinson, M. D. et al. (2016). Scientific Data, 3, 160018.
Notes: Teach students the heartbreak of lost field data and how strict daily triage saves research projects.

## Slide 30
MOD 4 • [CASESTUDY] • SLIDE 29/30
Case Study: Golden Grassland Cal/Val Campaign in California
CORE TAKEAWAY: The Jasper Ridge grassland field campaigns demonstrate how rigorous geometric protocols validate AVIRIS and PRISMA missions.
Target: Mediterranean annual grassland undergoing rapid summer dry-down.
Protocol: 100m × 100m grid with 49 sampling stations; ASD FieldSpec on 2.5m boom arm; RTK GPS coordinates.
Result: Characterized dry matter fraction (cellulose and lignin absorption at 2100 and 2300 nm) with R² = 0.89 against satellite retrievals.
Key success factor: Strict adherence to SZA < 40° window eliminated senescent canopy shadowing artifacts.
References: Gamon, J. A. et al. (1993). Functional patterns in an annual grassland during an AVIRIS overflight. Remote Sensing of Environment.
Notes: Show the Jasper Ridge spatial maps, hyperspectral image cubes, and the strong agreement with field spectra.

## Slide 31
MOD 4 • [PROTOCOL] • SLIDE 30/30
Module 4 Synthesis & Preparing for Hyperspectral Imaging
CORE TAKEAWAY: Flawless field protocols guarantee high-confidence ground truth data ready for scaling to UAV and satellite imaging platforms.
Module 4 synthesized: Solar zenith angle restrictions, BRDF avoidance, footprint calculations, operator exclusion, and ISO metadata.
In Module 5, we transition from single-point spectrometers to 2D hyperspectral and multispectral imaging: pushbroom cameras, UAV payloads, and image cubes.
Preparation for Field Exercise 4: Executing a full multi-point sampling grid over a heterogeneous vegetated parcel.
References: Milton, E. J. et al. (2009). Progress in field spectroscopy. Remote Sensing of Environment, 113, S92-S109.
Notes: Review the golden rules of field radiometry, answer questions on sampling geometry, and introduce Lab 4.