## Slide 1
PRINCIPLES OF FIELD SPECTROSCOPY • GEO-MSc-704
MODULE 5
UAV-Based Imaging Spectroscopy & Multispectral Payloads
4 Teaching Hours • 1.5 ECTS Credits • 30 Lecture Slides
Module 5 explores the operational and physical principles of airborne imaging spectroscopy deployed on Unmanned Aerial Vehicles (UAVs / drones). Students examine pushbroom (line-scan) spectrometers, 2D snapshot hyperspectral frame cameras, and multi-lens multispectral payloads (e.g. MicaSense RedEdge, DJI Mavic 3M, Headwall Nano-Hyperspec). The module covers direct georeferencing via tactical-grade GNSS/IMU integration, lever-arm and boresight calibration, rolling vs global shutter distortions, downwelling light sensors (DLS), lens vignetting correction, and the Empirical Line Method (ELM) using ground radiometric calibration tarps.

## Slide 2
MOD 5 • [INSTRUMENTATION] • SLIDE 1/30
Transition from Point Spectrometry to Drone Imaging Spectroscopy
CORE TAKEAWAY: UAV imaging spectroscopy bridges the spatial scaling gap between individual ground point spectra and satellite pixel grids.
Point spectrometers deliver exceptional spectral fidelity (> 2000 contiguous bands) but lack continuous spatial context.
Unmanned Aerial Vehicles (UAVs / drones) provide centimetric ground sampling distance (GSD 1–5 cm) with hundreds of spectral channels.
Enables mapping individual plant crowns, crop stress micro-heterogeneity, and sub-meter geological outcrops.
FIELD PROTOCOL NOTE
UAV flights inherit aircraft attitude dynamics (roll, pitch, yaw) and vibration requiring high-grade IMU integration.
References: Aasen, H. et al. (2018). Quantitative remote sensing at ultra-high resolution with UAV photogrammetry and spectroscopy. Remote Sensing.
Notes: Welcome to Module 5. We transition from stationary tripods to airborne drone imaging systems.

## Slide 3
MOD 5 • [INSTRUMENTATION] • SLIDE 2/30
Anatomy of Hyperspectral Sensor Types: Pushbroom vs. Snapshot
CORE TAKEAWAY: Pushbroom sensors scan linear cross-track swaths over time; snapshot frame cameras capture full 2D spatial images instantaneously.
Pushbroom (Line-scan, e.g. Headwall Nano-Hyperspec, Corning microHSI): Entrance slit disperses light along a 2D focal plane array (one spatial axis, one spectral axis). Forward aircraft motion builds the 2D image.
Snapshot Hyperspectral (e.g. Cubert UHD, Photonfocus): Captures 2D spatial dimensions (X, Y) and multiple spectral bands simultaneously in a single exposure.
Fabry-Perot Interferometer (FPI, e.g. Senop): Sequentially changes interferometer cavity gap to acquire spectral frames across time.
References: Adão, T. et al. (2017). Hyperspectral imaging: A review on UAV-based sensors, data processing and applications for agriculture and forestry. Remote Sensing.
Notes: Show the 3D data cube animation illustrating line-scan vs frame-sequential acquisition.

## Slide 4
MOD 5 • [INSTRUMENTATION] • SLIDE 3/30
Multispectral vs. Hyperspectral UAV Payloads
CORE TAKEAWAY: Multispectral sensors use discrete optical bandpass filters; hyperspectral sensors sample contiguous continuous narrow bands.
Multispectral (e.g. MicaSense RedEdge-P, DJI Mavic 3M): 5 to 10 broad bands (FWHM 10–40 nm) targeting key pigments and red edge.
Hyperspectral (e.g. Headwall, Resonon): 100 to 300+ contiguous narrow bands (FWHM 2–6 nm) resolving narrow absorption features.
Trade-off: Multispectral is lightweight, low-cost, and robust; hyperspectral is heavy, expensive, and demands complex georeferencing.
FIELD PROTOCOL NOTE
Multispectral sensors suffice for general NDVI and canopy vigor; hyperspectral is required for biochemical trait retrieval (nitrogen, carotenoids, lignin).
References: Zarco-Tejada, P. J. et al. (2012). High-resolution airborne hyperspectral imagery for assessing crop water stress. Agricultural and Forest Meteorology.
Notes: Display spectral band comparisons of MicaSense 5-band vs Headwall 270-band curves over the same leaf.

## Slide 5
MOD 5 • [PHYSICS] • SLIDE 4/30
The Pushbroom Image Cube Formation Physics
CORE TAKEAWAY: Pushbroom cameras project a single geographic line onto a 2D detector array, with one dimension recording space and the orthogonal dimension recording wavelength.
Spatial dimension: Line of N pixels across track (e.g. 640 or 1024 spatial pixels).
Spectral dimension: M spectral channels dispersed by an internal convex grating onto M rows of the array (e.g. 270 bands).
Frame rate (fps): The drone must fly forward at an exact ground speed to produce square pixels on the ground without spatial stretching or compression.
MATHEMATICAL FORMULATION
V_{\text{drone}} = \text{GSD} \cdot f_{\text{frame}} = \left( \frac{h \cdot p}{f} \right) \cdot f_{\text{frame}}
Ideal flight speed V_drone as a function of ground sampling distance GSD and camera frame rate f_frame.
References: Headwall Photonics (2018). Nano-Hyperspec User and Integration Manual.
Notes: Work out a practical flight calculation: if GSD = 3 cm and frame rate = 100 Hz, maximum flight speed is 3.0 m/s.

## Slide 6
MOD 5 • [INSTRUMENTATION] • SLIDE 5/30
Direct Georeferencing: GNSS/IMU Inertial Navigation
CORE TAKEAWAY: Pushbroom lines cannot be stitched using standard photogrammetry; each scan line requires position and orientation from an RTK GNSS/IMU.
Each individual pushbroom line is acquired at a unique microsecond in time with distinct aircraft roll, pitch, yaw, and altitude.
Applanix APX or SBG Ellipse tactical-grade Inertial Measurement Unit (IMU): Measures angular velocity and linear acceleration at 200–500 Hz.
Extended Kalman Filter (EKF): Fuses dual-frequency RTK GNSS and IMU gyroscopes to achieve pitch/roll accuracy < 0.03° and heading < 0.08°.
FIELD PROTOCOL NOTE
Never fly pushbroom payloads with consumer-grade IMUs; uncorrected roll wiggles turn straight crop rows into oscillating sine waves.
References: Mostafa, M. M. R., & Schwarz, K. P. (2000). A multi-sensor system for airborne mapping without ground control points. Photogrammetric Engineering & Remote Sensing.
Notes: Show the raw distorted "snake" pushbroom image before IMU trajectory correction and the clean orthorectified image after.

## Slide 7
MOD 5 • [QUALITYASSURANCE] • SLIDE 6/30
Boresight and Lever-Arm Calibration
CORE TAKEAWAY: Physical offsets between GNSS antenna, IMU center of navigation, and camera focal point must be calibrated to sub-millimeter precision.
Lever-Arm Offset [ΔX, ΔY, ΔZ]: Physical vector between IMU center of navigation and camera optical entrance pupil.
Boresight Misalignment Angles [dRoll, dPitch, dYaw]: Angular rotation between the IMU coordinate axes and the camera optical frame.
Calibration flights: Flying reciprocal opposing flight lines over distinct sharp control targets (buildings, survey markers) resolves boresight angles.
MATHEMATICAL FORMULATION
\mathbf{r}_{\text{ground}} = \mathbf{r}_{\text{GNSS}} + \mathbf{R}_{\text{IMU}} \cdot \mathbf{l}_{\text{lever}} + s \cdot \mathbf{R}_{\text{IMU}} \cdot \mathbf{R}_{\text{boresight}} \cdot \mathbf{u}_{\text{pixel}}
Rigorous direct georeferencing transformation equation.
References: Skaloud, J. (1999). Optimizing Direct Georeferencing of Airborne Mapping Systems. PhD Thesis, University of Calgary.
Notes: A boresight pitch error of only 0.2° produces a 17 cm ground projection error from a flight altitude of 50 m.

## Slide 8
MOD 5 • [PROCESSING] • SLIDE 7/30
Structure-from-Motion (SfM) Photogrammetry for Multispectral Frame Cameras
CORE TAKEAWAY: Snapshot and multispectral frame cameras reconstruct 3D surface geometry and orthomosaics using bundle block adjustment.
Scale-Invariant Feature Transform (SIFT): Detects thousands of shared feature keypoints across overlapping photos.
High overlap requirement: Multispectral mapping requires 75–85% forward overlap and 70–80% side overlap.
Bundle adjustment: Simultaneously solves camera interior orientation (focal length, lens distortion) and exterior poses.
Generates 3D Dense Point Cloud, Digital Surface Model (DSM), and radiometrically calibrated orthomosaic.
References: Westoby, M. J. et al. (2012). ‘Structure-from-Motion’ photogrammetry: A low-cost, effective tool for geoscience applications. Geomorphology.
Notes: Discuss Agisoft Metashape and Pix4D workflows for multispectral radiometric calibration.

## Slide 9
MOD 5 • [INSTRUMENTATION] • SLIDE 8/30
Downwelling Light Sensors (DLS / Sunshine Sensors)
CORE TAKEAWAY: Upward-looking DLS sensors measure incident solar irradiance during flight to normalize image pixels for solar illumination drift.
Mounted on the highest point of the UAV airframe with an unobstructed 180° hemispherical view of the sky.
Internal spectral photodiode channels matched to the camera bands, equipped with cosine diffusers.
Logs instantaneous solar irradiance for every captured image frame.
Correction model: Reflectance = (Pixel Radiance / Downwelling Irradiance) · Calibration Scale.
FIELD PROTOCOL NOTE
Propeller shadows passing over the DLS sensor create massive periodic irradiance noise spikes. Mount DLS on an elevated mast.
References: MicaSense Inc. (2020). RedEdge-P and DLS-2 Integration and Calibration Guide.
Notes: Show the MicaSense DLS-2 sensor and discuss how its built-in magnetometer and orientation sensor correct for drone tilt.

## Slide 10
MOD 5 • [QUALITYASSURANCE] • SLIDE 9/30
The Empirical Line Method (ELM) with Ground Calibration Tarps
CORE TAKEAWAY: ELM establishes a linear regression between in-flight digital numbers (or at-sensor radiance) and ground-measured surface reflectance.
Deploy at least two (optimally three or four) large Lambertian calibration tarps in the flight area.
Tarps: Typically 3% (black), 24% (medium gray), 48% (light gray), and 84% (white) diffuse reflectance across 400–1000 nm.
Tarps must be measured on the ground during flight with a calibrated point spectroradiometer (ASD or SVC).
ELM regression: ρ(λ) = Gain(λ) · DN(λ) + Offset(λ), directly accounting for atmospheric path radiance and sensor gain.
MATHEMATICAL FORMULATION
\rho_i(\lambda) = m(\lambda) \cdot \text{DN}_i(\lambda) + b(\lambda)
Empirical Line Method linear transfer equation.
FIELD PROTOCOL NOTE
Tarp size must span at least 5 to 10 image pixels to avoid mixed-edge adjacency effects.
References: Smith, G. M., & Milton, E. J. (1999). The use of the empirical line method to calibrate remotely sensed data to reflectance. IJRS.
Notes: Point out why ELM remains the gold standard for UAV optical calibration: it eliminates atmospheric model uncertainties.

## Slide 11
MOD 5 • [INSTRUMENTATION] • SLIDE 10/30
Rolling Shutter vs. Global Shutter Distortions
CORE TAKEAWAY: Rolling shutters expose pixels line-by-line, causing severe "jello" geometric warping during UAV flight motion; global shutters are mandatory.
Rolling shutter: CMOS array reads out top-to-bottom sequentially over several milliseconds.
High-frequency drone vibrations and forward velocity shear and warp objects within a single frame.
Global shutter: All photodiode wells open and close simultaneously, freezing the entire spatial scene instantaneously.
Never use consumer rolling-shutter cameras for precision quantitative radiometry.
References: Vautherin, J. et al. (2016). Photogrammetric accuracy and modeling of rolling shutter cameras on UAVs. ISPRS Annals.
Notes: Show the classic rolling shutter photo of a bent airplane propeller to explain why it destroys photogrammetric geometry.

## Slide 12
MOD 5 • [PROCESSING] • SLIDE 11/30
Optical Vignetting and Lens Falloff Correction
CORE TAKEAWAY: Optical vignetting causes image brightness to decay radial-symmetrically from the optical center toward the frame corners.
Cosine-fourth law of illumination: Off-axis image brightness drops with cos⁴(θ_lens).
Mechanical vignetting: Lens barrel or filter rims physically obstructing peripheral light rays.
Calibration: Laboratory flat-field acquisition using an integrating sphere or uniform white light panel.
Vignetting lookup table (LUT): Multiplies corner pixels by inverse radial falloff polynomial V(r) = 1 + k₁·r² + k₂·r⁴.
MATHEMATICAL FORMULATION
I_{\text{corrected}}(x, y) = \frac{I_{\text{raw}}(x, y)}{V(r)}, \quad r = \sqrt{(x - x_0)^2 + (y - y_0)^2}
Radial flat-field vignetting normalization formula.
References: Kelcey, J., & Lucieer, A. (2012). Sensor correction of a 6-band multispectral imaging sensor for UAV remote sensing. Remote Sensing.
Notes: Show an uncorrected multispectral mosaic with dark circular halos in every frame before vignetting correction.

## Slide 13
MOD 5 • [INSTRUMENTATION] • SLIDE 12/30
Gimbal Stabilization: 3-Axis Brushless Gimbals vs. Fixed Mounts
CORE TAKEAWAY: Active 3-axis brushless gimbals decouple camera orientation from aircraft buffeting, maintaining true nadir pointing.
High-torque brushless motors and dedicated IMU controllers compensate for drone roll, pitch, and yaw in milliseconds.
Fixed camera mounts inherit every tilt of the drone, causing footprint wander of ±15° during windy cross-tracks.
In pushbroom imaging, gimbals maintain the scan line perpendicular to the flight path vector.
FIELD PROTOCOL NOTE
Balance the gimbal mechanically with power OFF until the camera sits neutral in any orientation before powering motors.
References: Aasen, H. et al. (2018). Remote Sensing.
Notes: Show how an unbalanced gimbal overheats its motor drivers and induces high-frequency micro-jitter.

## Slide 14
MOD 5 • [MATHEMATICS] • SLIDE 13/30
Ground Sampling Distance (GSD) & Flight Altitude Math
CORE TAKEAWAY: Ground Sampling Distance represents the physical ground dimension represented by a single detector pixel.
GSD is governed by flight altitude h above ground level (AGL), camera focal length f, and sensor pixel pitch p.
Higher altitude expands field coverage but degrades spatial resolution.
In undulating terrain, GSD varies across the flight line unless terrain-following flight planning is utilized.
MATHEMATICAL FORMULATION
\text{GSD} = \frac{h \cdot p}{f} \iff h = \frac{\text{GSD} \cdot f}{p}
Fundamental photogrammetric ground sampling distance equation.
References: Wolf, P. R. et al. (2014). Elements of Photogrammetry with Applications in GIS (4th ed.). McGraw-Hill.
Notes: Calculate GSD for a 5.5 µm pixel pitch, 8 mm lens flown at 50 m AGL (GSD = 50 * 5.5e-6 / 8e-3 = 3.44 cm).

## Slide 15
MOD 5 • [PROTOCOL] • SLIDE 14/30
Terrain Following Flight Planning with High-Resolution DEMs
CORE TAKEAWAY: Flying at fixed barometric altitude over hilly terrain causes massive variations in GSD and overlap, ruining orthomosaics.
Barometric altimeters maintain fixed height relative to takeoff point, not local ground level.
Flying over a 50m hill from a 80m takeoff drops true altitude to 30m, causing image overlap to plunge and risking terrain collision.
Terrain following: Flight management software (e.g. UgCS, DJI Pilot) adjusts drone altitude dynamically using an onboard Digital Elevation Model (SRTM, LiDAR).
FIELD PROTOCOL NOTE
Always verify terrain DEM accuracy; outdated SRTM data may miss new quarry pits or tree canopy heights.
References: Nex, F., & Remondino, F. (2014). UAV for 3D mapping applications: a review. Applied Geomatics.
Notes: Show the flight profile cross-section of a terrain-following flight vs a flat barometric flight.

## Slide 16
MOD 5 • [PHYSICS] • SLIDE 15/30
Atmospheric Path Radiance and Adjacency Effects at UAV Altitudes
CORE TAKEAWAY: At 50–120 m flight altitudes, atmospheric attenuation is small (< 2–3%) but target adjacency and diffuse scattering still exist.
Unlike 700 km satellites, UAVs operate beneath 99% of the atmospheric column.
Rayleigh scattering in the 50 m path is negligible (< 0.5% in blue).
However, dense haze or dust plumes create significant path radiance.
Adjacency effect: Photons reflected from bright concrete borders scatter into adjacent dark vegetation pixels.
References: Bimonte, M. et al. (2021). Atmospheric correction of UAV hyperspectral data. Remote Sensing.
Notes: Explain why full atmospheric radiative transfer codes like 6S/MODTRAN are usually overkill for low-altitude UAVs, whereas ELM is ideal.

## Slide 17
MOD 5 • [PHYSICS] • SLIDE 16/30
Signal-to-Noise Ratio (SNR) in Airborne Imaging Systems
CORE TAKEAWAY: Airborne imaging spectrometers suffer lower SNR than ground point sensors due to millisecond integration times and tiny pixel areas.
Ground point spectrometer: Big entrance slit, large foreoptic, integration times 10–100 ms, SNR > 1000:1.
UAV pushbroom pixel: Tiny entrance slit, fast flight speed requiring integration times 2–5 ms, SNR often 100:1 to 300:1.
Binning (spatial and spectral): Summing adjacent pixels 2×2 or 4×4 boosts SNR at the expense of spatial or spectral resolution.
MATHEMATICAL FORMULATION
\text{SNR}_{\text{binned}} = \text{SNR}_0 \cdot \sqrt{N_{\text{pixels}}}
SNR scaling through hardware pixel binning.
References: Schaepman, M. E. (2007). Spectroradiometry—A review. Remote Sensing of Environment.
Notes: Highlight this core trade-off: You cannot have 1 cm spatial resolution, 1 nm spectral resolution, and 1000:1 SNR simultaneously on a drone.

## Slide 18
MOD 5 • [PROTOCOL] • SLIDE 17/30
Solar Angle Restrictions & Glint in UAV Surveys
CORE TAKEAWAY: UAV surveys over wet soils, rice paddies, or water bodies produce intense specular sun glint that saturates camera arrays.
Sun glint: Direct mirror reflection of the solar disk into the wide-angle camera lens.
Occurs when surface normal bisects the sun and sensor vectors (Snell-Fresnel specular geometry).
Polarized lens filters and off-nadir camera tilting (10°–15° away from solar azimuth) eliminate specular glint.
Over land, solar zenith angle must remain between 30° and 50° to avoid both deep tree shadows and extreme hotspot surge.
References: Suomalainen, J. et al. (2014). Direct reflectance measurements from drones. Remote Sensing.
Notes: Show a multispectral orthomosaic over an orchard where half the leaves are washed out white from sun glint.

## Slide 19
MOD 5 • [QUALITYASSURANCE] • SLIDE 18/30
Calibration Panel Deployment & Ground Target Protocols
CORE TAKEAWAY: Calibration tarps must be maintained in pristine condition and pinned flat to prevent wind flutter and shadow folds.
Position tarps in an open, level area free from building or tree shadows throughout the flight.
Anchor tarp corners with tent pegs to eliminate wind billowing.
Measure the center of each tarp with a calibrated field spectroradiometer at the exact moment the UAV passes overhead.
Never walk on or drag equipment across radiometric calibration tarps.
FIELD PROTOCOL NOTE
Store calibration tarps rolled around PVC cores; folding tarps creates permanent creases that cause micro-shadows.
References: Smith, G. M., & Milton, E. J. (1999). International Journal of Remote Sensing.
Notes: Show photos of well-pinned tarps versus wrinkled, windblown tarps that ruined a drone survey.

## Slide 20
MOD 5 • [PROTOCOL] • SLIDE 19/30
UAV Flight Mission Design & Overlap Strategies
CORE TAKEAWAY: Mission geometry must guarantee consistent ground overlap, cross-track coverage, and adequate battery reserves.
Flight lines: Parallel serpentine paths oriented perpendicular to prevailing wind to maintain steady ground speed.
Forward overlap (along-track): 80% minimum for multispectral SfM matching in vegetated canopies.
Side overlap (cross-track): 75% minimum to prevent longitudinal stitching seams and gaps.
Battery reserve: Plan flight duration to land with at least 25% battery capacity remaining.
FIELD PROTOCOL NOTE
Repetitive agricultural crops (wheat, maize) lack visual texture; insufficient overlap (< 75%) causes photogrammetry alignment failure.
References: Aasen, H. et al. (2018). Remote Sensing.
Notes: Demonstrate flight planning in software, showing overlap coverage heatmaps.

## Slide 21
MOD 5 • [PROCESSING] • SLIDE 20/30
Radiometric Calibration Pipelines in Photogrammetry Suites
CORE TAKEAWAY: Modern photogrammetry suites (Agisoft Metashape, Pix4D) execute multi-stage radiometric calibration algorithms.
Stage 1: Read EXIF metadata (exposure time, ISO gain, sensor black level, calibration panel albedo).
Stage 2: DLS solar irradiance normalization frame-by-frame.
Stage 3: Lens vignetting and radial distortion removal.
Stage 4: Calibration panel optimization (ELM calibration factor calculation).
Output: 16-bit or 32-bit floating-point GeoTIFF reflectance orthomosaics scaled from 0.0 to 1.0.
References: Pix4D SA (2020). Radiometric Calibration of Multispectral Images Technical Guide.
Notes: Walk students through the radiometric calibration settings panel in Pix4Dmapper and Agisoft Metashape.

## Slide 22
MOD 5 • [CASESTUDY] • SLIDE 21/30
Multi-Sensor Payloads: Thermal IR and LiDAR Co-Registration
CORE TAKEAWAY: Fusing hyperspectral imagery with concurrent UAV LiDAR and thermal infrared provides structural and physiological data.
UAV LiDAR: Delivers 3D structural canopy height models (CHM), vertical vegetation density profiles, and exact ground terrain.
Thermal IR (e.g. FLIR Vue Pro R): Measures canopy surface kinetic temperature, revealing stomatal conductance and early water stress.
Hyperspectral: Delivers biochemical pigment concentrations (chlorophyll, carotenoids, nitrogen).
Spatial co-registration: Merging LiDAR point clouds with hyperspectral voxels creates true 3D hyper-spectral canopy models.
References: Zarco-Tejada, P. J. et al. (2013). Assessing vineyard water status with UAV thermal and hyperspectral imagery. Remote Sensing of Environment.
Notes: Show a 3D LiDAR canopy point cloud color-coded by hyperspectral chlorophyll content.

## Slide 23
MOD 5 • [QUALITYASSURANCE] • SLIDE 22/30
UAV Regulatory Frameworks & Airspace Safety Protocols
CORE TAKEAWAY: Scientific UAV operations require strict adherence to national civil aviation authorities (FAA Part 107, EASA Open/Specific Category).
Pilot-in-Command (PIC) certification: Mandatory commercial remote pilot licensing.
Visual Line-of-Sight (VLOS): Drone must remain visible to the remote pilot without visual aids at all times.
Maximum altitude ceiling: Typically 120 m (400 ft) AGL to avoid manned general aviation airspace.
Pre-flight risk assessment: Failsafe return-to-home (RTH) programming, lost-link procedures, and emergency landing zones.
FIELD PROTOCOL NOTE
Always conduct a physical crew safety briefing and test RTH altitude settings before taking off.
References: FAA (2021). 14 CFR Part 107 — Small Unmanned Aircraft Systems. Federal Aviation Administration.
Notes: Review the legal liabilities of conducting university UAV research flights.

## Slide 24
MOD 5 • [QUALITYASSURANCE] • SLIDE 23/30
Data Volumes, Storage Architecture & Field Compute
CORE TAKEAWAY: UAV hyperspectral surveys generate massive data volumes (50–200 GB per flight) requiring high-throughput field storage.
A 20-minute pushbroom flight collecting 100 frames/sec at 1024 spatial pixels × 270 bands generates ~35 GB of raw uncompressed data.
Field requirements: Fast NVMe solid-state drives (read/write > 1500 MB/s) to offload flight cards quickly.
Field triage workstation: High-core laptop with GPU acceleration to inspect pushbroom track completeness before leaving the field.
FIELD PROTOCOL NOTE
Never fly subsequent missions using the same SD card without verifying full hash-verified checksum backup.
References: Aasen, H. et al. (2018). Remote Sensing.
Notes: Calculate daily storage requirements for a 4-flight research campaign.

## Slide 25
MOD 5 • [QUALITYASSURANCE] • SLIDE 24/30
Quality Assessment of UAV Orthomosaics
CORE TAKEAWAY: Systematic QA checks must verify radiometric uniformity, spatial resolution, and geometric positional accuracy.
Ground Control Points (GCPs): Independent check points surveyed with RTK-GNSS must yield RMSE_xy < 1–2 GSD.
Radiometric uniformity: Verify that no striping or brightness seams exist along flight line boundaries.
Ghosting and blur: Inspect moving vegetation in the mosaic for double edges or motion-blur artifacts caused by wind.
References: Turner, D. et al. (2012). An automated technique for generating georeferenced orthorectified mosaics from ultra-high resolution UAV imagery. IEEE TGRS.
Notes: Show examples of poor orthomosaic stitching where tree crowns are smeared into blurred artifacts.

## Slide 26
MOD 5 • [CASESTUDY] • SLIDE 25/30
Case Study: Precision Viticulture Water Stress Mapping
CORE TAKEAWAY: Airborne multispectral imagery at 5 cm GSD isolates pure grapevine sunlit leaves from shaded soil and grass cover.
Vineyard challenge: Conventional 10m satellite pixels mix vine rows (30%), bare soil (50%), and inter-row weed grass (20%).
UAV solution: 5 cm multispectral orthomosaic allows automated mask segmentation isolating 100% pure vine canopies.
Photochemical Reflectance Index (PRI) and CWSI (Crop Water Stress Index) retrieved from pure vine pixels correlate with leaf water potential (R² = 0.84).
References: Zarco-Tejada, P. J. et al. (2013). Remote Sensing of Environment.
Notes: Display the high-resolution vine segmentation mask and the resulting water stress prescription map.

## Slide 27
MOD 5 • [CASESTUDY] • SLIDE 26/30
Case Study: Forest Canopy Biodiversity and Tree Species Classification
CORE TAKEAWAY: UAV hyperspectral imaging identifies tropical and temperate tree species by resolving subtle biochemical absorption signatures.
Individual Tree Crown (ITC) delineation using high-resolution canopy height models.
Extraction of 150-band continuous spectral signatures per individual tree crown.
Machine learning classification (Support Vector Machines, Random Forest) achieves > 92% tree species identification accuracy.
Distinguishes ash, oak, beech, and birch based on red edge slopes and water overtone band depths.
References: Féret, J. B., & Asner, G. P. (2013). Tree species discrimination in tropical forests using airborne imaging spectroscopy. IEEE TGRS.
Notes: Show the classified forest map with individual delineated crowns color-coded by species.

## Slide 28
MOD 5 • [CASESTUDY] • SLIDE 27/30
Case Study: Acid Mine Drainage & Heavy Metal Soil Contamination
CORE TAKEAWAY: UAV pushbroom spectroscopy maps iron oxide mineralogy (hematite, goethite, jarosite) across mine tailings at sub-meter scale.
Acid mine drainage generates distinctive secondary iron sulfate and oxide precipitates.
Jarosite (diagnostic absorption at 430 nm and 2260 nm) indicates highly acidic conditions (pH < 3).
Goethite (absorption at 480 nm and 900 nm) indicates neutralizing pH conditions.
UAV mapping pinpoints active acid generation zones without hazardous foot sampling in toxic tailings ponds.
References: Swayze, G. A. et al. (2000). Using imaging spectroscopy to map acidic mine waste. Environmental Science & Technology.
Notes: Present the geological false-color composite and mineral abundance maps from an abandoned copper mine.

## Slide 29
MOD 5 • [CASESTUDY] • SLIDE 28/30
Cross-Scale Validation: Ground Point to Drone to Satellite
CORE TAKEAWAY: UAV imaging spectroscopy serves as the critical intermediate upscaling bridge validating spaceborne missions (PRISMA, EnMAP, EMIT).
Tier 1 (Ground): ASD point spectrometer characterizes leaf optics and calibration tarps with SI traceability.
Tier 2 (Airborne): UAV hyperspectral camera maps 1 km² area at 5 cm GSD, capturing full spatial variability.
Tier 3 (Spaceborne): Convolving UAV mosaic to 30m EnMAP/PRISMA pixels provides synthetic validation scenes with zero spatial error.
References: Kokaly, R. F. et al. (2009). Spectroscopic remote sensing for material identification and mapping. Remote Sensing of Environment.
Notes: Show the multi-tier scaling pyramid diagram from leaf clip to space station sensor.

## Slide 30
MOD 5 • [INSTRUMENTATION] • SLIDE 29/30
Emerging Sensor Horizons: Lightweight SWIR and Hyperspectral LiDAR
CORE TAKEAWAY: Miniaturized SWIR pushbroom cameras (1000–2500 nm) and hyperspectral LiDAR are opening revolutionary new observational dimensions.
SWIR on drones: Historically prohibited by weight (> 10 kg); new compact InGaAs cameras weigh < 1.8 kg.
Enables airborne mineral mapping, cellulose/lignin detection, and microplastic identification on drones.
Hyperspectral LiDAR (Supercontinuum laser): Measures range and contiguous reflectance simultaneously, delivering illuminated spectra without solar shadows.
References: Hakala, T. et al. (2012). Full waveform hyperspectral LiDAR for remote sensing of vegetation. Optics Express.
Notes: Preview the cutting-edge prototypes currently in academic flight testing.

## Slide 31
MOD 5 • [INSTRUMENTATION] • SLIDE 30/30
Module 5 Synthesis & Progression to Spectral Preprocessing
CORE TAKEAWAY: UAV spectroscopy demands mastery of sensor physics, direct IMU georeferencing, ELM tarp calibration, and photogrammetry.
Module 5 established: Pushbroom vs snapshot sensors, IMU trajectory synchronization, GSD math, ELM tarp calibration, and flight planning.
In Module 6, we analyze spectral curves mathematically: Savitzky-Golay smoothing, SNV, continuum removal, derivatives, and spectral indices.
Preparation for Field Exercise 5: Conducting an airborne multispectral drone flight with ground calibration tarps and ASD validation.
References: Aasen, H. et al. (2018). Quantitative remote sensing with UAV spectroscopy. Remote Sensing.
Notes: Wrap up UAV lecture, address flight planning questions, and preview Practical Lab 5.