## Slide 1
PRINCIPLES OF FIELD SPECTROSCOPY • GEO-MSc-704
MODULE 6
Advanced Spectral Preprocessing, Continuum Removal & Feature Extraction
4 Teaching Hours • 1.5 ECTS Credits • 30 Lecture Slides
Module 6 equips MSc students with advanced mathematical and chemometric algorithms for preprocessing field spectra and extracting diagnostic biochemical and mineralogical features. The curriculum covers noise suppression via Savitzky-Golay polynomial convolution, scatter correction via Standard Normal Variate (SNV) and Multiplicative Scatter Correction (MSC), and the Clark & Roush continuum removal algorithm. Students derive physical absorption metrics: band center, band depth, FWHM, and absorption band area. The module explores spectral derivatives (1st/2nd order, red edge inflection point REIP), narrow-band physiological indices (PRI, NDRE, CI_RE, NDWI, CAI), and dimensionality reduction via PCA, MNF, and Partial Least Squares Regression (PLSR).

## Slide 2
MOD 6 • [PROCESSING] • SLIDE 1/30
Introduction to Spectral Preprocessing & Feature Extraction
CORE TAKEAWAY: Raw reflectance curves contain both diagnostic chemical absorption features and confounding multiplicative scatter noise.
Physical scatter vs. Chemical absorption: Particle size, leaf internal cell anatomy, and surface roughness induce baseline shifts.
Preprocessing objective: Remove non-linear scattering and instrument noise while enhancing subtle molecular vibrational and electronic transitions.
Core methods: Smoothing, scatter correction (SNV, MSC), continuum removal, derivative spectroscopy, and narrow-band indices.
FIELD PROTOCOL NOTE
Never apply chemometric modeling (PLSR, Random Forest) directly to raw un-preprocessed field spectra.
References: Rinnan, Å. et al. (2009). Review of the most common pre-processing techniques for near-infrared spectra. TrAC Trends in Analytical Chemistry.
Notes: Welcome to Module 6. Here we master the mathematical toolkit of chemometrics and spectroscopic feature extraction.

## Slide 3
MOD 6 • [MATHEMATICS] • SLIDE 2/30
Noise Suppression: Moving Average vs. Gaussian vs. Savitzky-Golay
CORE TAKEAWAY: Simple moving averages distort narrow absorption peak shapes; Savitzky-Golay filters preserve peak height, width, and area.
Moving average: Replaces each point with the unweighted local mean; flattens sharp absorption peaks and widens FWHM.
Gaussian filter: Applies Gaussian weights; still attenuates high-frequency peak tips.
Savitzky-Golay (1964): Fits a local polynomial of degree p across a moving window of 2m + 1 points using least-squares convolution coefficients.
MATHEMATICAL FORMULATION
y_j^* = \sum_{i=-m}^m c_i \cdot y_{j+i}
Savitzky-Golay convolution sum where c_i are precomputed least-squares polynomial coefficients.
References: Savitzky, A., & Golay, M. J. (1964). Smoothing and differentiation of data by simplified least squares procedures. Analytical Chemistry.
Notes: Demonstrate on the board how a moving average blunts a sharp Kaolinite doublet into an uninterpretable lump.

## Slide 4
MOD 6 • [MATHEMATICS] • SLIDE 3/30
Savitzky-Golay Parameter Optimization: Window Size & Polynomial Degree
CORE TAKEAWAY: Selecting the optimal window length and polynomial order requires balancing noise removal against spectral feature distortion.
Polynomial degree p: Typically quadratic (p=2) or cubic (p=3); higher degrees (p=4, 5) fit high-frequency noise.
Window size w = 2m + 1: Must be odd and smaller than the full width at half maximum (FWHM) of the narrowest diagnostic absorption feature.
If window size exceeds absorption feature FWHM, the feature is systematically smoothed away.
Rule of thumb: In field spectroscopy with 1 nm sampling, w = 11 to 21 points (11 to 21 nm) with polynomial degree 2 or 3.
References: Schafer, R. W. (2011). What is a Savitzky-Golay filter? IEEE Signal Processing Magazine.
Notes: Show the effect of increasing window size from 5 to 51 nm on the Chlorophyll red edge slope.

## Slide 5
MOD 6 • [MATHEMATICS] • SLIDE 4/30
Standard Normal Variate (SNV) Transformation
CORE TAKEAWAY: SNV centers and scales each individual spectrum independently, eliminating additive baseline offsets and multiplicative scaling effects.
Developed by Barnes et al. (1989) for near-infrared diffuse reflectance spectroscopy of particulates.
Additive shift: Caused by sample height variations and stray light.
Multiplicative scaling: Caused by particle size differences and optical path length changes.
SNV requires no reference or target set; it operates on a single spectrum row-by-row.
MATHEMATICAL FORMULATION
x_{ij}^{\text{SNV}} = \frac{x_{ij} - \bar{x}_i}{s_i}, \quad \bar{x}_i = \frac{1}{K}\sum_{k=1}^K x_{ik}, \quad s_i = \sqrt{\frac{1}{K-1}\sum_{k=1}^K (x_{ik} - \bar{x}_i)^2}
Standard Normal Variate normalization for spectrum i at channel j across K wavelengths.
References: Barnes, R. J. et al. (1989). Standard normal variate transformation and de-trending of near-infrared diffuse reflectance spectra. Applied Spectroscopy.
Notes: Point out that after SNV, every spectrum has a mean of 0.0 and a standard deviation of 1.0.

## Slide 6
MOD 6 • [MATHEMATICS] • SLIDE 5/30
Multiplicative Scatter Correction (MSC)
CORE TAKEAWAY: MSC separates light scattering from chemical absorption by regressing each spectrum against an ideal reference mean spectrum.
Formulated by Geladi et al. (1985).
Assumes that physical scatter linearly shifts and scales the entire spectrum relative to an average population spectrum.
Step 1: Compute the mean spectrum x̄ across the entire calibration dataset.
Step 2: Fit linear regression per spectrum: x_i = a_i + b_i · x̄ + e_i.
Step 3: Correct spectrum: x_i^MSC = (x_i - a_i) / b_i.
MATHEMATICAL FORMULATION
x_i(\lambda) = a_i + b_i \cdot \bar{x}(\lambda) + e_i(\lambda) \implies x_i^{\text{MSC}}(\lambda) = \frac{x_i(\lambda) - a_i}{b_i}
MSC linear scatter correction equation.
References: Geladi, P. et al. (1985). Linearization and scatter-correction for near-infrared reflectance spectra of meat. Applied Spectroscopy.
Notes: Contrast MSC with SNV: MSC uses the population mean; SNV is purely sample-internal. Their results are mathematically very similar.

## Slide 7
MOD 6 • [MATHEMATICS] • SLIDE 6/30
Detrending Algorithms: Removing Baseline Curvature
CORE TAKEAWAY: Detrending fits a second-order polynomial baseline to each spectrum, removing curvilinear drift caused by dense scattering.
Often applied immediately following SNV (SNV-Detrending pipeline).
Accounts for wavelength-dependent scattering that increases at shorter wavelengths (Rayleigh-Mie scatter curvature).
Fits y = c₀ + c₁·λ + c₂·λ² to the SNV-transformed curve and subtracts the fitted curve.
Flattens spectral baselines to zero, highlighting discrete absorption bands.
References: Barnes, R. J. et al. (1989). Applied Spectroscopy.
Notes: Show an agricultural grain flour spectrum before and after SNV-Detrend.

## Slide 8
MOD 6 • [MATHEMATICS] • SLIDE 7/30
Continuum Removal: The Convex Hull Concept
CORE TAKEAWAY: Continuum removal normalizes reflectance spectra to a common convex hull baseline, isolating true absorption band shapes.
Formalized by Clark & Roush (1984) at USGS Spectroscopy Lab.
Continuum: An upper boundary convex hull that connects local reflectance maxima, representing background scattering without absorption.
Mathematical definition: Smallest convex polygon enclosing all spectral points from above.
Continuum-removed reflectance: Ratio of original reflectance to the continuum value at each wavelength: R_cr(λ) = R(λ) / R_c(λ).
MATHEMATICAL FORMULATION
R_{\text{cr}}(\lambda) = \frac{R(\lambda)}{R_c(\lambda)} \quad \implies \quad 0.0 \le R_{\text{cr}}(\lambda) \le 1.0
Continuum-removed reflectance is bounded between 0 (complete absorption) and 1 (on the continuum baseline).
References: Clark, R. N., & Roush, T. L. (1984). Reflectance spectroscopy: Quantitative analysis techniques for remote sensing applications. JGR.
Notes: Draw the rubber-band analogy on the board: imagine stretching a rubber band tightly over the top of the spectral curve.

## Slide 9
MOD 6 • [MATHEMATICS] • SLIDE 8/30
Continuum-Removed Diagnostic Parameters
CORE TAKEAWAY: Continuum-removed features yield quantitative physical parameters: Band Center, Band Depth, FWHM, and Absorption Area.
Band Center (λ_min): Wavelength corresponding to minimum continuum-removed reflectance (maximum absorption).
Band Depth (BD): Maximum absorption depth: BD = 1.0 - R_cr(λ_min).
Full Width at Half Maximum (FWHM): Width of the absorption feature where depth is half of BD: BD / 2.
Absorption Band Area: Numerical integral of (1.0 - R_cr(λ)) across the absorption interval.
MATHEMATICAL FORMULATION
\text{BD} = 1 - R_{\text{cr}}(\lambda_{\min}), \quad \text{Area} = \int_{\lambda_{\text{start}}}^{\lambda_{\text{end}}} \left(1 - R_{\text{cr}}(\lambda)\right) \, d\lambda
Band Depth and Band Area definitions for quantitative absorption feature characterization.
References: Clark, R. N. (1999). Manual of Remote Sensing.
Notes: Demonstrate how Band Area scales linearly with chemical absorber concentration according to radiative transfer theory.

## Slide 10
MOD 6 • [MATHEMATICS] • SLIDE 9/30
Absorption Feature Asymmetry and Skewness
CORE TAKEAWAY: Absorption feature asymmetry reveals overlapping secondary absorption sub-bands and mineral solid solutions.
Symmetric feature: The left half-width (λ_min - λ_left) equals the right half-width (λ_right - λ_min).
Asymmetry parameter: S = (λ_right - λ_min) / (λ_min - λ_left) or S = log((Area_right) / (Area_left)).
In Kaolinite vs Halloysite: Asymmetry distinguishes disorder in the crystal lattice.
In chlorophyll: Carotenoid absorption on the left wing (450–500 nm) creates strong negative asymmetry.
MATHEMATICAL FORMULATION
\text{Asymmetry} = \frac{\lambda_{\text{right, 0.5}} - \lambda_{\min}}{\lambda_{\min} - \lambda_{\text{left, 0.5}}}
Ratio of right to left half-width at half-maximum depth.
References: Van der Meer, F. (2004). Analysis of spectral absorption features. International Journal of Applied Earth Observation.
Notes: Show the Al-OH 2200 nm feature in pure muscovite vs phengite and how asymmetry shifts.

## Slide 11
MOD 6 • [MATHEMATICS] • SLIDE 10/30
Spectral Derivatives: First and Second Order Formulations
CORE TAKEAWAY: Spectral derivatives eliminate baseline offsets (1st derivative) and linear slopes (2nd derivative), resolving overlapping peaks.
First Derivative (dR/dλ): Measures spectral slope. Zero-crossings locate reflectance peaks and absorption troughs.
Second Derivative (d²R/dλ²): Measures curvature. Negative values identify local maxima; positive peaks identify absorption minima.
Derivative computation: Implemented simultaneously with Savitzky-Golay polynomial differentiation to suppress noise amplification.
MATHEMATICAL FORMULATION
\frac{d R}{d\lambda} \approx \frac{R(\lambda_{i+1}) - R(\lambda_{i-1})}{2 \Delta\lambda}, \quad \frac{d^2 R}{d\lambda^2} \approx \frac{R(\lambda_{i+1}) - 2R(\lambda_i) + R(\lambda_{i-1})}{(\Delta\lambda)^2}
Central finite difference approximations for first and second derivatives.
References: Tsai, F., & Philpot, W. (1998). Derivative analysis of hyperspectral data. Remote Sensing of Environment.
Notes: Warning: Taking a numerical derivative of raw noisy data amplifies high-frequency noise by 1/Δλ. Always smooth first!

## Slide 12
MOD 6 • [MATHEMATICS] • SLIDE 11/30
The Red Edge Inflection Point (REIP) Algorithms
CORE TAKEAWAY: REIP marks the maximum first-derivative slope between red chlorophyll absorption (680 nm) and the NIR plateau (750 nm).
Guyot & Baret (1988) 4-band linear interpolation model.
Miller et al. (1990) inverted-Gaussian fitting model.
First-derivative peak detection: Finding the exact wavelength where dR/dλ reaches its maximum.
Chlorophyll increase causes the REIP to shift toward longer wavelengths ("red edge shift") due to saturation of the 680 nm band.
MATHEMATICAL FORMULATION
\lambda_{\text{REIP}} = 700 + 40 \cdot \left[ \frac{\frac{R_{670} + R_{780}}{2} - R_{700}}{R_{740} - R_{700}} \right]
Guyot & Baret (1988) formulation for Red Edge Position from four spectral bands.
References: Guyot, G., & Baret, F. (1988). Utilisation de la haute résolution spectrale pour suivre l'état des couverts végétaux. ESA SP-287.
Notes: Show the red edge shift in leaves subjected to heavy metal stress vs healthy controls.

## Slide 13
MOD 6 • [MATHEMATICS] • SLIDE 12/30
Broadband vs. Narrowband Spectral Indices
CORE TAKEAWAY: Narrowband indices exploit specific 2–5 nm physical absorption features, avoiding saturation common in broadband indices.
Broadband indices (e.g. Landsat NDVI): Integrate 50–100 nm chunks; saturate rapidly at LAI > 2.5 to 3.0.
Narrowband indices (hyperspectral): Select precise wavelengths on the red edge slope, xanthophyll cycle, or water overtones.
Red Edge NDVI (NDRE): Replaces red band with red edge band (705 nm), maintaining sensitivity at high biomass (LAI > 6.0).
References: Gitelson, A. A., & Merzlyak, M. N. (1994). Quantitative estimation of chlorophyll-a content in plant leaves using reflectance spectra. Journal of Photochemistry and Photobiology.
Notes: Compare the saturation curve of broadband NDVI vs narrowband NDRE over a dense corn canopy.

## Slide 14
MOD 6 • [PROCESSING] • SLIDE 13/30
Pigment Indices: Chlorophyll, Carotenoids & Anthocyanins
CORE TAKEAWAY: Tailored band ratios isolate specific pigment pools without interference from overlapping absorption.
Chlorophyll Index Red Edge: CI_RE = (R780 / R710) - 1.0 (linear relationship with foliar chlorophyll content).
Chlorophyll Index Green: CI_Green = (R780 / R550) - 1.0.
Carotenoid Reflectance Index (CRI550): CRI = (1 / R510) - (1 / R550).
Anthocyanin Reflectance Index (ARI): ARI = (1 / R550) - (1 / R700).
MATHEMATICAL FORMULATION
\text{CI}_{\text{RE}} = \frac{R_{780}}{R_{710}} - 1, \quad \text{ARI} = \frac{1}{R_{550}} - \frac{1}{R_{700}}
Gitelson pigment indices based on reciprocal reflectance differences.
References: Gitelson, A. A. et al. (2006). Novel algorithms for remote estimation of vegetation fraction. Remote Sensing of Environment.
Notes: Explain the three-band concept: 1/R(pigment) - 1/R(interfering) normalized by R(NIR).

## Slide 15
MOD 6 • [PHYSICS] • SLIDE 14/30
Photochemical Reflectance Index (PRI) & Xanthophyll Cycle
CORE TAKEAWAY: PRI tracks the rapid, reversible epoxidation of violaxanthin to antheraxanthin and zeaxanthin in the photosynthetic apparatus.
Xanthophyll cycle: Non-Photochemical Quenching (NPQ) dissipates excess absorbed photon energy as heat under stress.
Induces a subtle 0.2% to 0.5% absorption shift at 531 nm.
Reference band at 570 nm is unaffected by xanthophyll interconversion.
PRI = (R531 - R570) / (R531 + R570): Directly correlates with light use efficiency (LUE) and diurnal photosynthetic stress.
MATHEMATICAL FORMULATION
\text{PRI} = \frac{R_{531} - R_{570}}{R_{531} + R_{570}}
Formulated by Gamon et al. (1992) for diurnal tracking of photosynthetic efficiency.
FIELD PROTOCOL NOTE
Requires high SNR instruments; changes in PRI are small and easily drowned out by instrument drift.
References: Gamon, J. A., Peñuelas, J., & Field, C. B. (1992). A narrow-waveband spectral index that tracks diurnal changes in photosynthetic efficiency. RSE.
Notes: Show diurnal PRI curves: drops sharply at midday as plants enter photo-inhibition, recovers in late afternoon.

## Slide 16
MOD 6 • [PROCESSING] • SLIDE 15/30
Canopy Water Indices: WI, NDWI & NDII
CORE TAKEAWAY: Water indices exploit weak water overtone absorption features at 970 nm and 1240 nm to retrieve canopy moisture.
Water Index (WI): WI = R900 / R970 (Peñuelas et al., 1993).
Normalized Difference Water Index (NDWI): NDWI = (R860 - R1240) / (R860 + R1240) (Gao, 1996).
Normalized Difference Infrared Index (NDII): NDII = (R860 - R1640) / (R860 + R1640).
Directly estimates Equivalent Water Thickness (EWT [g/cm²]) and Fuel Moisture Content (FMC %).
MATHEMATICAL FORMULATION
\text{WI} = \frac{R_{900}}{R_{970}}, \quad \text{NDWI} = \frac{R_{860} - R_{1240}}{R_{860} + R_{1240}}
Formulations for foliar water overtone retrieval.
References: Gao, B. C. (1996). NDWI—A normalized difference water index for remote sensing of vegetation liquid water from space. RSE.
Notes: Why use 970 and 1240 nm rather than 1400 nm? Because 1400 nm saturates immediately and is blocked by atmosphere.

## Slide 17
MOD 6 • [PHYSICS] • SLIDE 16/30
Cellulose Absorption Index (CAI) & Non-Photosynthetic Vegetation (NPV)
CORE TAKEAWAY: CAI quantifies dry plant litter, crop residue, and dead senescent vegetation using cellulose and lignin features in the SWIR.
Crop residue and dry grass cannot be detected with NDVI because chlorophyll is gone.
Cellulose and lignin exhibit diagnostic doublet absorption features at 2100 nm and 2300 nm.
CAI = 0.5 · (R2000 + R2200) - R2100 (Daughtry, 2001).
Essential for monitoring conservation tillage, carbon sequestration, and wildfire fuel loads.
MATHEMATICAL FORMULATION
\text{CAI} = 100 \cdot \left[ 0.5 \cdot (R_{2000} + R_{2200}) - R_{2100} \right]
Cellulose Absorption Index formulated by Daughtry (2001).
References: Daughtry, C. S. (2001). Discriminating crop residues from soil by shortwave infrared reflectance. Agronomy Journal.
Notes: Show the SWIR spectrum of dry wheat straw vs green wheat vs bare mineral soil.

## Slide 18
MOD 6 • [PROCESSING] • SLIDE 17/30
Mineral Indices: Clay, Carbonate & Iron Oxide Ratios
CORE TAKEAWAY: Narrowband SWIR band ratios differentiate clay species, carbonate rocks, and iron oxide alteration phases.
Al-OH Hydroxyl Index (Kaolinite/Muscovite): (R2160 / R2200).
Carbonate Index (Calcite/Dolomite): (R2340 / R2200).
Ferrous Iron Index: R1600 / R900.
Ferric Oxide Index (Hematite vs Goethite): R650 / R450 and 2nd derivative zero-crossings.
References: Ninomiya, Y. et al. (2005). Detecting lithology with advanced spaceborne thermal emission and reflection radiometer (ASTER). RSE.
Notes: Show how mining geologists use these exact band ratios to map alteration zones in real time.

## Slide 19
MOD 6 • [MATHEMATICS] • SLIDE 18/30
Spectral Angle Mapper (SAM) & Spectral Correlation Measure (SCM)
CORE TAKEAWAY: SAM treats spectra as vectors in N-dimensional space, measuring spectral angle θ independent of illumination brightness.
Vector dot product: cos(θ) = (t · r) / (||t|| · ||r||).
Spectral angle θ is invariant to uniform illumination scaling (shadows or irradiance changes).
Spectral Correlation Measure (SCM): Computes Pearson correlation coefficient r between target and reference spectrum.
SCM standardizes spectra to mean 0, variance 1, making it robust against additive baseline offsets.
MATHEMATICAL FORMULATION
\theta(\mathbf{t}, \mathbf{r}) = \arccos\left( \frac{\sum_{i=1}^B t_i r_i}{\sqrt{\sum_{i=1}^B t_i^2} \sqrt{\sum_{i=1}^B r_i^2}} \right)
Spectral Angle Mapper angle in radians or degrees.
References: Kruse, F. A. et al. (1993). The spectral image processing system (SIPS)—Interactive visualization and analysis. RSE.
Notes: Explain the geometric intuition: Two spectra that have identical shapes but differ in brightness lie along the same vector ray (θ = 0).

## Slide 20
MOD 6 • [MATHEMATICS] • SLIDE 19/30
Spectral Information Divergence (SID)
CORE TAKEAWAY: SID models spectra as probability distributions and calculates spectral similarity using Kullback-Leibler information divergence.
Formulated by Chang (2000) based on Shannon information theory.
Normalizes spectrum to a probability vector: p_i = x_i / Σ x_k.
Calculates relative entropy D(p || q) and symmetrizes: SID = D(p || q) + D(q || p).
More sensitive to subtle narrow absorption feature differences than SAM.
MATHEMATICAL FORMULATION
\text{SID}(\mathbf{p}, \mathbf{q}) = \sum_{i=1}^B p_i \log\left(\frac{p_i}{q_i}\right) + \sum_{i=1}^B q_i \log\left(\frac{q_i}{p_i}\right)
Symmetric Kullback-Leibler spectral information divergence.
References: Chang, C. I. (2000). An information-theoretic approach to spectral variability, similarity, and discrimination for hyperspectral imagery. IEEE TGRS.
Notes: Compare classification confusion matrices of SAM vs SID for discriminating 12 mineral species.

## Slide 21
MOD 6 • [MATHEMATICS] • SLIDE 20/30
Principal Component Analysis (PCA) on Hyperspectral Data
CORE TAKEAWAY: PCA transforms hundreds of correlated spectral channels into an uncorrelated orthogonal subspace, concentrating variance.
Hyperspectral bands exhibit severe multicollinearity (> 0.95 inter-band correlation between adjacent channels).
PCA diagonalizes the spectral covariance matrix: C = V · Λ · Vᵀ.
First 3 to 5 Principal Components typically capture > 98% of total spectral variance across the dataset.
PC1 captures overall brightness/albedo; PC2 captures red-edge/pigment contrast; PC3 captures SWIR moisture/cellulose.
Noise whitening: Higher-order PCs contain primarily random noise and can be truncated.
References: Richards, J. A. (2013). Remote Sensing Digital Image Analysis (5th ed.). Springer.
Notes: Show the scree plot of eigenvalues and display false-color composites of PC1, PC2, and PC3.

## Slide 22
MOD 6 • [MATHEMATICS] • SLIDE 21/30
Minimum Noise Fraction (MNF) Transformation
CORE TAKEAWAY: MNF performs two cascaded PCA rotations: the first separates and whitens noise; the second concentrates signal-to-noise ratio.
Standard PCA orders components by total variance, which can mistakenly elevate high-variance noise.
MNF (Green et al., 1988) orders components strictly by Signal-to-Noise Ratio (SNR).
Requires an estimate of the noise covariance matrix (from dark scans or spatial shift differences).
Coherent vs. Noise bands: Eigenvalues >> 1 contain coherent spatial/spectral signal; eigenvalues near 1 contain pure white noise.
References: Green, A. A. et al. (1988). A transformation for ordering multispectral data in terms of image quality with implications for noise removal. IEEE TGRS.
Notes: Contrast MNF with PCA. Explain why MNF is the standard preprocessing step prior to spectral unmixing.

## Slide 23
MOD 6 • [MATHEMATICS] • SLIDE 22/30
Linear Spectral Mixture Analysis (LSMA) & Endmember Extraction
CORE TAKEAWAY: Field footprints often mix multiple surface covers; LSMA decomposes mixed spectra into fractional abundances of pure endmembers.
Linear mixture model: Mixed spectrum is the linear combination of pure endmembers weighted by their areal fractions: x = Σ f_k · e_k + ε.
Physical constraints: Fully Constrained Least Squares (FCLS): Abundance Non-Negativity Constraint (f_k ≥ 0) and Sum-to-One Constraint (Σ f_k = 1).
Endmember extraction algorithms: Pixel Purity Index (PPI), N-FINDR, Vertex Component Analysis (VCA).
MATHEMATICAL FORMULATION
\mathbf{x} = \sum_{k=1}^P f_k \mathbf{e}_k + \boldsymbol{\varepsilon}, \quad \text{s.t.} \; f_k \ge 0 \; \text{and} \; \sum_{k=1}^P f_k = 1
Fully Constrained Linear Spectral Mixture Model.
References: Adams, J. B., Smith, M. O., & Gillespie, A. R. (1993). Imaging spectroscopy: Interpretation based on spectral mixture analysis. Remote Geochemical Analysis.
Notes: Walk students through unmixing a mixed pixel containing 40% green leaf, 35% dry litter, and 25% bare soil.

## Slide 24
MOD 6 • [PHYSICS] • SLIDE 23/30
Non-Linear Spectral Mixing in Vegetation Canopies
CORE TAKEAWAY: Multiple scattering between canopy leaves and background soil produces non-linear photon interactions that violate linear mixture models.
Linear mixing assumes photons interact with only one surface component before entering the foreoptic.
In dense canopies, transmitted NIR photons bounce between multiple leaf layers and soil before exitance.
Hapke intimate mixture model and bilinear models (Fan, Nascimento) account for multi-bounce interactions.
Linear unmixing of vegetation canopies typically overestimates soil fraction if non-linear scattering is ignored.
References: Ray, T. W., & Murray, B. C. (1996). Nonlinear spectral mixing in desert vegetation. RSE.
Notes: Draw the multiple scattering photon trajectory through a 3D forest canopy to explain non-linear mixing.

## Slide 25
MOD 6 • [MATHEMATICS] • SLIDE 24/30
Partial Least Squares Regression (PLSR) in Spectroscopy
CORE TAKEAWAY: PLSR projects both predictor spectra (X) and target biochemical traits (Y) to latent variables, maximizing covariance.
Overcomes multicollinearity where ordinary least squares (OLS) regression completely fails.
Latent vectors: Supervised decomposition that extracts features most predictive of foliar nitrogen, phosphorus, or LMA.
Cross-validation (k-fold or leave-one-out): Determines the optimal number of latent components to avoid overfitting.
Variable Importance in Projection (VIP): Identifies which spectral wavelengths contribute most to the biochemical model.
References: Wold, S. et al. (2001). PLS-regression: a basic tool of chemometrics. Chemometrics and Intelligent Laboratory Systems.
Notes: Explain VIP scores: Wavelengths with VIP > 1.0 are considered statistically significant predictors.

## Slide 26
MOD 6 • [QUALITYASSURANCE] • SLIDE 25/30
Cross-Validation & Avoiding Overfitting in Chemometrics
CORE TAKEAWAY: With 2000 spectral predictor bands and 50 field samples, random correlation can produce spurious R² > 0.95 without cross-validation.
The Curse of Dimensionality: p >> n problem (more spectral bands than physical ground samples).
Always evaluate models on an independent holdout test set (e.g. 70% train / 30% test).
Spatial cross-validation: Split training and testing sets by geographic spatial blocks to avoid spatial autocorrelation leakage.
Report RMSE_CV (Cross-Validation Root Mean Square Error) and RPD (Ratio of Performance to Deviation).
FIELD PROTOCOL NOTE
Never report calibration R² alone; report validation R²_val and RMSE_val on truly independent sites.
References: Roberts, D. R. et al. (2017). Cross-validation strategies for data with spatial, temporal, hierarchical or phylogenetic structure. Ecography.
Notes: Show an example of a 100-band noise dataset predicting a random coin flip with R² = 0.92 when overfitted with OLS.

## Slide 27
MOD 6 • [CASESTUDY] • SLIDE 26/30
Automated Spectral Feature Matching: USGS Tetracorder
CORE TAKEAWAY: USGS Tetracorder matches unknown field spectra against a reference spectral library using continuum-removed shape metrics.
Developed by Roger Clark and USGS Spectral Lab team.
Normalizes candidate features using continuum removal over diagnostic wavelength intervals.
Computes weighted correlation coefficient, band depth, and asymmetry against > 1000 laboratory reference minerals and plants.
Delivers automated mineral identification with quantitative confidence levels.
References: Clark, R. N. et al. (2003). Imaging spectroscopy: Earth and planetary remote sensing with the USGS Tetracorder and expert systems. JGR.
Notes: Show the USGS mineral library database and the Tetracorder decision-tree logic flow.

## Slide 28
MOD 6 • [CASESTUDY] • SLIDE 27/30
Foliar Nitrogen & Protein Retrieval: The N-H SWIR Bands
CORE TAKEAWAY: Foliar nitrogen is bound primarily in Rubisco enzymes and photosynthetic proteins, producing diagnostic N-H absorption in SWIR.
Total leaf nitrogen (N %): Highly correlated with maximum carboxylation rate (Vcmax) and photosynthetic capacity.
N-H peptide bond absorption features: 1510 nm, 1680 nm, 2060 nm, and 2180 nm.
Often masked by liquid water in fresh leaves; continuum removal and first-derivative analysis isolate protein features.
PLSR models routinely achieve R² > 0.85 for nitrogen retrieval across diverse plant functional types.
References: Kokaly, R. F. (2001). Investigating a physical basis for spectroscopic estimates of canopy nitrogen concentration. RSE.
Notes: Show dry leaf spectra vs fresh leaf spectra in the 2100–2200 nm zone to demonstrate protein feature unmasking.

## Slide 29
MOD 6 • [PROCESSING] • SLIDE 28/30
Open-Source Spectral Processing Toolkits: Python & R Ecosystem
CORE TAKEAWAY: The modern spectroscopic research workflow is built on open-source Python (pysptools, specdal, scikit-learn) and R (hsdar, prospectr).
Python: `pysptools` (endmember extraction, unmixing), `specdal` (instrument readers, ASD batch processing), `scikit-learn` (PLSR, PCA, RF).
R: `hsdar` (hyperspectral data analysis, PROSAIL coupling, indices), `prospectr` (SNV, MSC, Savitzky-Golay, continuum removal).
Guarantees fully scripted, reproducible, version-controlled scientific analysis pipelines.
References: Lehnert, L. W. et al. (2019). hsdar: Manage, analyze and simulate hyperspectral data in R. Package Vignette.
Notes: Review the package dependencies and show the online documentation for hsdar and prospectr.

## Slide 30
MOD 6 • [QUALITYASSURANCE] • SLIDE 29/30
Batch Processing Pipelines for Large Field Campaigns
CORE TAKEAWAY: Automated batch pipelines enforce consistent quality flags, dark current subtraction, and feature extraction across thousands of spectra.
Modular pipeline architecture: Ingestion -> Quality screening -> Dark current subtract -> White reference calibrate -> Saturated band mask -> Savitzky-Golay filter -> Continuum removal -> Feature extraction -> Export to SPECCHIO / NetCDF.
Automated logging of QA failure flags (e.g. WR departure > 1.5%, SZA > 50°).
Enables repeatable re-processing when sensor calibration coefficients are updated.
References: Hueni, A. et al. (2009). Computers & Geosciences.
Notes: Show the flowchart of an automated batch script processing 5,000 field spectra in under 2 minutes.

## Slide 31
MOD 6 • [PROCESSING] • SLIDE 30/30
Module 6 Synthesis & Preparing for Radiative Transfer Modeling
CORE TAKEAWAY: Preprocessing and feature extraction isolate fundamental physical and biochemical parameters from noisy outdoor spectra.
Module 6 established: Savitzky-Golay smoothing, SNV, MSC, continuum removal convex hulls, band depths, derivatives, and spectral indices.
In Module 7, we explore the forward physics: Radiative Transfer Models (RTMs) spanning leaf-level PROSPECT and canopy-level SAIL (PROSAIL) and look-up table inversion.
Preparation for Field Exercise 6: Collecting leaf and mineral spectra and executing continuum removal and band depth analysis.
References: Clark, R. N., & Roush, T. L. (1984). JGR, 89(B7), 6329-6340.
Notes: Wrap up preprocessing lecture, confirm understanding of continuum removal math, and introduce Lab 6.